## Slide 1: New Physical Layer Paradigm for Future Systems: Moving away from orthogonality to save energy and bandwidth
Professor Izzat Darwazeh
Director of UCL Institute of Communications and Connected Systems (ICCS)
University College London, UK
WWRF 47
Bristol June 2022

## Slide 2: “New” Physical Layer Paradigm for Future Systems: Moving away from orthogonality to save energy and bandwidth
Professor Izzat Darwazeh
Director of UCL Institute of Communications and Connected Systems (ICCS)
University College London, UK
MAP-tele Workshop
University of the Minho-Braga-September 2021

## Slide 3: Why does radio/modulation change from generation to generation?
We would like radio signals that can carry all the information, maintaining data quality , integrity and security in smallest possible bandwidth and lowest possible energy using simplest equipment.
Use: think of 1G, GSM, UMTS and then LTE and 5G
Data rate: kb/s to Gb/s
Bandwidth and radio
Signal quality and errors:
  Channel physics: delay spread, environment, user speed
  Channel use: noise and interference
Equipment, energy and complexity

## Slide 4: Why does radio/modulation change from generation to generation?
We would like radio signals that can carry all the information, maintaining data quality , integrity and security in smallest possible bandwidth and lowest possible energy using simplest equipment.
FM GMSK CDMA/QAM OFDM/QAM
Use: think of 1G, GSM, UMTS and then LTE and 5G
Data rate: kb/s to Gb/s
Bandwidth and radio
Radio signals and specterum make all the difference

## Slide 5
OFDM concept has not changed since 1958!!
A binary bit stream is divided into N-binary bit streams.
Bit duration is extended from Tb to N x Tb
What does this do to the spectrum?
Each of the N sub-streams modulates a sinusoidal carrier known as (sub-carrier)
The carriers are at different frequencies and are separated by
Δf = 1/N x Tb
The sub-streams are added together and transmitted

## Slide 6
The concept has not changed since 1958!!
This is an FSK system, but a special one!!
Total BW 2090 + 110 = 2200 Hz
20 sub-carriers
Sub-carrier separation = 110 Hz
= 1/18.2 ms

## Slide 7
OFDM circa 1959
R. Mosier and R. Clabaugh, Kineplex, a bandwidth efficient binary transmission system, AIEE Proceedings, Vol. 76, January 1958

## Slide 8
Parallel Communications methods are not new!!

## Slide 9: Orthogonal FDM

## Slide 10
LTE and 5GNR
Where else is OFDM used?
System | Transform Size | Number Carriers | Channel Spacing kHz | Bandwidth MHz | Sample Rate MHz | Symbol Duration sec | Data Rate Mbits/s
HyperLAN/2 | 64 | 52 4 | 312.5 | 16.25 | 20 | 3.2 0.8 | 6-54
802.11a | 64 | 52 4 | 312.5 | 16.56 | 20 | 3.2 0.8 | 6-54
DVB-T | 2048 1024 | 1712 842 | 4.464 | 7.643 | 9.174 | 224 | 0.68-14.92
DAB | 2048 8192 | 1536 | 1.00 | 1.536 | 2.048 | 24/48/96 msec | 3.072
ADSL | 256 (down) 64 (up) | 36-127 7-28 | 4.3125 | 1.104 | 1.104 | 231.9 | 0.64-8.192

## Slide 11
Minimum Shift Keying
(Basis of GSM signals)
Used in GSM

## Slide 12: Think of something in between

## Slide 13: The non-orthogonal signal waveform
OFDM (12 sub-carriers, data rate is 𝑅𝑏).
SEFDM Type-I (12 sub-carriers, bandwidth compression factor 𝛼=0.67, data rate is 𝑅𝑏).
SEFDM Type-II (12 sub-carriers, bandwidth compression factor 𝛼=0.67, data rate is 1.5𝑅𝑏).
Bandwidth saving
Connection increase
Data rate increase
OFDM-no saving

## Slide 14: Mutistream Faster Than Nyquist (FTN) (D. Dasalukunte, F. Rusek, and V. Owall, “An iterative decoder for multicarrier faster-than-Nyquist signaling systems,” in Communications (ICC), 2010 IEEE International Conference on, May 2010, pp. 1–5)
FTN: increase spectral efficiency by transmitting data faster than Nyquist criterion.

## Slide 15: SEFDM: Spectrally Efficient FDM
Bandwidth ≈ B Hz
No ICI
Modulation: OFDM
Total QPSK symbol rate: B Baud (Symbol/s)
Bandwidth ≈ α∙B Hz, 0<α<1
With ICI
Bandwidth Saving vs. ICI
Modulation: SEFDM
Total QPSK symbol rate: B Baud (Symbol/s)

## Slide 16: And in 1975…

## Slide 17: IMT 2030

## Slide 18: Challenges
Does it work over different media (wireless and optical)?
Can it be made? SDR techniques; FPGAs; ICs
Practical problems?
Signal generation
Signal detection
Channel estimation
RF engineering, Amplifiers and mm-wave
Synchronisation
Frequency and phase offsets
Coding and FEC
Interference cancellation
Fit within existing standard waveforms and frames
Offer advantages over existing systems in real environments

## Slide 19: PAPR advantage
Safa Isam and Izzat Darwazeh “Peak to average power ratio reduction in spectrally efficient FDM systems” 18th International Conference on Telecommunications, 2011
Notes: Abstract:Spectrally efficient FDM (SEFDM) systems are new and attractive multicarrier systems that can significantly enhance spectral utilization. However, as a multicarrier system SEFDM is prone to high peak to average power ratio (PAPR). In this work we present for the first time a study of the PAPR in SEFDM systems. We explore the performance of standard PAPR reduction techniques and propose a novel PAPR reduction algorithm, based on sliding a time window across an extended SEFDM symbol period, therefore termed the SLiding Window (SLW) PAPR reduction technique. Numerical simulations confirm this new technique efficacy in PAPR reduction and show no side effects. Furthermore, a complete transmitter that employs SLW is proposed based on the SEFDM IDFT transmitter. SLW shows remarkable PAPR reduction with no spectral spreading or Bit Error Rate (BER) compromises at a much reduced complexity when compared to standard Partial Transmit Sequence (PTS) and Selective Mapping (SLM) PAPR reduction techniques.

## Slide 20: Simple signal generation using IFFT
SEFDM signal generation
Similar to OFDM signal generation
Padding zeros
IFFT is applicable to SEFDM

OFDM

SEFDM
(SigGen-I)
Truncate to N samples

## Slide 21: Customized Hardware Transmitter
Metric | Value
Analogue Bandwidth with buffering PER DAC (8 in total) | 150MHz
DAC Resolution | 16-Bit
Max SNR | 106dB
Max sample length/DAC | 300mS
Live streaming – 1 DAC Analogue bandwidth | 31.25MHz
Live streaming – 4 DAC Analogue Bandwidth | 7.125MHz
DAC’s
FPGA
DDR RAM
SPI
Power PCB
Ethernet
M R Perrett and I Darwazeh “Flexible hardware architecture of SEFDM transmitters with real-time non-orthogonal adjustment” 18th International Conference on Telecommunications, 2011, pp.369-374.
Notes: SPI: Serial Peripheral Interface

## Slide 22: VLSI Transmitter Implementation
Reconfigurable SEFDM modulator
32nm CMOS process
Throughput of 250 Mbps to 750 Mbps for QPSK – 64QAM
1mm
[1 ]. P. Whatmough, M. Perrett, S. Isam, and I. Darwazeh, “VLSI architecture for a reconfigurable spectrally efficient FDM baseband transmitter,” IEEE Transactions on Circuits and Systems I: , vol. 59, no. 5, pp. 1107 –1118, may 2012.

## Slide 23: FPGA Implementation of Real-Time Detectors
T. Xu, R. C. Grammenos, and I. Darwazeh, “FPGA implementations of real-time detectors for a spectrally efficient FDM system,” in Telecommunications (ICT), 2013 20th International Conference on, 2013, pp. 1–5.
Operation block diagram of TSVD-FSD

## Slide 24: BER performance of the TSVD-FSD-SF and TSVD-FSD-MNSF detector for 4QAM-SEFDM system with α=0.8,N=16,TW=16.
Virtex-6 FPGA
Occupied resource map
FPGA Implementations of Real-Time Detectors

## Slide 25: Channel Estimation: OFDM Pilots in SEFDM signals
(a) Time domain
(b) Frequency domain

## Slide 26: Implementation of real-time SEFDM system
OFDM pilot for channel estimation
Realistic channel and noise using channel emulator
A Pipeline design architecture for SEFDM iterative decoder
Real-time SEFDM using SDR platform (LabVIEW & USRP)
Ozan, Waseem, et al. “Experimental Evaluation of Channel Estimation and Equalisation in Non-Orthogonal FDM Systems." In 2018 11th International Symposium on CSNDSP, IEEE, 2018.
Ozan, Waseem, P. A. Haigh, B. Tan, and I. Darwazeh. “Experimental SEFDM pipelined iterative detection architecture with improved throughput." In 2018 IEEE 87th Vehicular Technology Conference (VTC Spring), pp. 1-5. IEEE, 2018.
Ozan, Waseem, H. Ghannam, P. A. Haigh, and I. Darwazeh. “Experimental implementation of real-time non-orthogonal multi-carrier systems in a realistic fading channel." In Radio and Wireless Symposium (RWS), IEEE, 2018.
Ozan, Waseem, R. Grammenos, H. Ghannam, P. A. Haigh, and I. Darwazeh. “Real-Time SEFDM Transceiver for 5G Systems and Beyond." Personal, Indoor, and Mobile Radio Communications (PIMRC), 2017 IEEE 28th Annual International Symposium on. IEEE, 2017.

## Slide 27: Implementation of real-time SEFDM system
Receiver Pipeline architecture for SEFDM system

## Slide 28: Introduction of zero padding in SEFDM systems
Ozan, Waseem, R. Grammenos, and I. Darwazeh. “Zero Padding or Cyclic Prefix: Evaluation for Non Orthogonal Signals.“ IEEE Communication Letters. IEEE, 2020.

## Slide 29: Can be viewed as truncated time domain signals
Advantages in WiFi environments with high interference

## Slide 30: Contribution #4 (1/2): Introduction of PSR to Operate Interfering Wireless Networks in Collision Environments
Developed the TOFDM concept to operate the current 802.11a,g systems successfully in collision environment
Presented a new receiver design termed Partial Symbol Recovery (PSR)
PSR: treats non- and partially-overlapping OFDM symbols differently
Designed and implemented the PSR receiver on WARP SDR platform
Region (a): Collision-free
Region (b): Two partially-overlapping symbols
Region (c): Completely overlapping symbols

## Slide 31: Networks in Collision Environments
Evaluated in 12-node SDR
Non-line-of-sight environment
Two-user data rate region, PSR operates beyond the SIC rate region
Decoding capability, on average 59% and 25% for BPSK and QPSK
Throughput performance, an enhancement of up to 21%
Retransmission performance, a reduction of up to 80%
Ozan, Waseem, I. Darwazeh, and K. Jamieson. “Shifting Perspective to Operate Interfering Wireless Networks Beyond Capacity.“ IEEE/ACM Transaction on Networking, IEEE/ACM, 2020. (under review)

## Slide 32: Wireless
The above experiment testbed is applicable to two scenarios:
LTE: Single band SEFDM (excluding zero insertion)
LTE-A: Carrier aggregation SEFDM (including zero insertion)
[1]. T. Xu and I. Darwazeh, “Bandwidth compressed carrier aggregation,” in IEEE ICC 2015 - Workshop on 5G & Beyond - Enabling Technologies and Applications (ICC’15 - Workshops 23), London, United Kingdom, Jun. 2015, pp. 1107–1112.
[2]. T. Xu and I. Darwazeh, “Practical Implementation of Bandwidth Compressed Carrier Aggregation in a Realistic Fading Channel,” IEEE Transactions on Vehicular Technology, Vol 65, Issue 5, May 2017
[3]. T. Xu and I. Darwazeh, “Nyquist-SEFDM: Pulse Shaped Sub-Carriers with Frequency Spacing Below the Symbol Rate,” in Wireless Communications and Networking Conference (WCNC), IEEE, 2016.
Notes: This practical idea is submitted to ICC 2015 workshop. 3026C is signal generator; 3035C is digitizer; 3010 is clock; VR5 is channel emulator.
We implemented two systems, one is a single band LTE-SEFDM, the other one is the LTE-Advanced carrier aggregation (CA)-SEFDM system. Both systems can reuse the above experimental setup except for the zero insertion module. This module is designed only for CA-SEFDM due to the protection band between adjacent component carriers (CC)

## Slide 33: Wireless: LTE format
Channel Equalization
OFDM
Channel Equalization
SEFDM
α=0.8
A static frequency selective channel is emulated.
Time-domain channel estimation and equalization
Notes: System specification is shown in the first table.
A static frequency selective channel is configured in the right table.
The top middle figure shows frame structure and resource grid structure.
Spectrum and constellation are measured at 36 dB.
One reference of time-domain channel estimation; constellation before and after channel equalization for OFDM and SEFDM (a=0.8); a time-domain channel estimation and equalization is shown above.
The unit of x-axis is MHz. The bottom left figure is OFDM (the bandwidth is 18.015 MHz), the bottom right is SEFDM (the bandwidth is 18.015*0.8=14.412 MHz).

## Slide 34
OFDM
α = 0.8
α = 0.6
Experimental picture transmission by using SEFDM signal (Eb/No=25 dB).
18 MHz
14.4 MHz
10.8 MHz
Notes: Image transmission through the predefined static frequency selective channel.
The right figures are practical spectra obtained from a spectrum analyzer. It should be noted that a normal spectrum is employed in Turbo-SEFDM system. It is different with B-SEFDM.

## Slide 35: Realistic channel (ETU70) measurements
The number of NB-IoT sub-carriers is 12 with each occupying 15 kHz and overall bandwidth is 180 kHz (one resource block).
For such a narrow band signal, frequency selective in one resource block exists.
No channel
ETU70-01
ETU70-02

## Slide 36
(a). Performance of different Turbo-SEFDM systems with various levels of bandwidth compressions in the RF environment with frequency selective channel. v is the number of iterations.
(b). Throughput of different Turbo-SEFDM systems computed based on the BER information in Fig (a) and system specifications. v is the number of iterations.
(c). CCDF of PAPR for SEFDM and OFDM systems modulated with 4QAM symbols.
Wireless: LTE
Notes: Throughput is calculated based on BER information and system specifications on page 20. we remove useless information like pilot symbols, CP, DC part, guard band and coding redundancy.

## Slide 37: SEFDM signal waveform
T. Xu and I. Darwazeh, “Transmission experiment of bandwidth compressed carrier aggregation in a realistic fading channel,” IEEE Transactions on Vehicular Technology, vol. 66, no. 5, pp. 4087–4097, May 2017.

## Slide 38: SEFDM with carrier aggregation)
(a). Performance of different CA-SEFDM systems in the condition of real RF environment with the LTE EPA5 fading channel.
(b). Effective spectral efficiency (bit/s/Hz) of different CA-SEFDM systems computed based on the BER information and the system specifications.
Data rates:
LTE: 50 Mbit/s
SEFDM: 70 Mbit/s
Realistic LTE defined multipath fading channel with 5 kHz Doppler spread is used.
Seven signal bands are aggregated in CA-SEFDM while five for CA-OFDM in the same bandwidth.
40% more data can be delivered using the CA-SEFDM scheme.

## Slide 39: Reconfigurable IFFT to Generate SEFDM 5G NR Signals
H. Ghannam and I. Darwazeh. A Proposal for Scalable 5G New Radio Frames with Enhanced Throughput. In IEEE 89th Vehicular Technology Conference (Spring), Kuala Lumpur, April 2019.

## Slide 40
Block Error Rate of Coexisting system employing LDPC
Figure 9: BLER performance for the coexisting systems in three scenarios using LDPC coding, N = 12, coding rate 1/3
Xinyue Liu;Tongyang Xu and Izzat Darwazeh,
“Coexistence of Orthogonal and Non-orthogonal Multicarrier Signals in Beyond 5G Scenarios
2020 2nd 6G Wireless Summit (6G SUMMIT),

## Slide 41: Complex modulation and probabilistic shaped SEFDM Use of ML on 5G-like signals to design signal, modulation and constellation

## Slide 42: Same bandwidth but higher rate, probabilistic shaping improves efficiency
X. Liu etal, Spectrally Efficient FDM System with Probabilistic Shaping, submitted to VTC fall (in May 2021)

## Slide 43: Fast-OFDM signal waveform A simple format, half the bandwidth and IoT applications and for VLC
M. R. D. Rodrigues and I. Darwazeh, “Fast OFDM: A proposal for doubling the data rate of OFDM schemes” Proceedings of the IEEE/IEE International Conference on Telecommunications (ICT 2002), vol. 3, pp. 484-487, Beijing, China, June 2002. (invited paper)
T. Xu and I. Darwazeh, “Non-orthogonal narrowband Internet of Things: A design for saving bandwidth and doubling the number of connected devices,” IEEE Internet of Things Journal, vol. 5, no. 3, pp. 2120–2129, Jun. 2018.
P. A. Haigh, A. Burton, Z. Ghassemlooy, I. Darwazeh, “Visible Light Communications: Simplified Co-Equalisation of Fast OFDM in a Multiple-Input Multiple-Output Configuration”, International Telecommunications Conference (ICT), April 2019, Hanoi-Vietnam.

## Slide 44: Direct Detection Optical-SEFDM
Electrical spectrum
Optical spectrum
I. Darwazeh, T. Xu, T. Gui, Y. Bao, and Z. Li, “Optical SEFDM system; bandwidth saving using non-orthogonal sub-carriers,” Photonics Technology Letters, IEEE, vol. 26, no. 4, pp. 352–355, Feb 2014
 Bandwidth compression of electrical spectrum saves protection gap in optical spectrum

## Slide 45
Data rate = 10 Gbit/s.
Modulation: 4QAM, 8QAM
Number of subcarrier = 16.
Cyclic prefix: 1/16
Bandwidth compression factor α= 0.7, 0.75, 0.80, 0.9 and 1.
Direct Detection Optical-SEFDM
 World first practical nonorthogonal system experiment (2013)
4QAM-SEFDM (SE=2.86 bit/s/Hz) outperforms 8QAM-OFDM (SE=3 bit/s/Hz) by 1.6 dB
B2B
80 km

## Slide 46: SEFDM over optical channels
Experimental setup of PDM-CO-SEFDM transmission system
[1]. D. Nopchinda, T. Xu, R. Maher, B. Thomsen, and I. Darwazeh, ”Dual polarization coherent optical spectrally efficient frequency division multiplexing,” Photonics Technology Letters, IEEE, vol. 28, no. 1, pp. 83–86, Jan 2016.
Notes: A detailed description of the experiment setup is referred to the un-submitted CO-SEFDM PTL paper.

## Slide 47: Optical: Coherent
24 Gbit/s 4QAM
BER as a function of OSNR, B2B (left) and 80 km link
D. Nopchinda, T. Xu, R. Maher, B. Thomsen, and I. Darwazeh, “Dual polarization coherent optical spectrally efficient frequency division multiplexing,” IEEE Photonics Technology Letters, vol. 28, no. 1, pp. 83–86, Jan 2016.
50% bit rate increase
3.5dB power penalty

## Slide 48: 60 GHz Millimeter Wave Communication
T. Xu, S. Mikroulis, J. E. Mitchell, and I. Darwazeh, “Bandwidth compressed waveform for 60-GHz millimeter-wave radio over fiber experiment,” Journal of Lightwave Technology, vol. 34, no. 14, pp. 3458–3465, July 2016.
60 GHz parabolic antennas have 30 dBi gain; and 3 dB beamwidth of 3.1◦ are employed.
A 30 dB gain high power amplifier (HPA) at the transmitter and a 30 dB gain low noise amplifier (LNA) at the receiver.
Transmission distances from few cm to 3 metres.

## Slide 49: Experimental results for the 60 GHz mm-wave SEFDM-2
BER measurements
Iteration study
OFDM: no iteration.
SEFDM: at least one iteration.
Within the same bandwidth, bit rate can be increased by up to 67%.
4QAM α=0.67 outperforms the 8QAM OFDM have the same spectral efficiency. SEFDM has with 1 dB performance gain.
The 4QAM α=0.6 outperforms the 8QAM OFDM in both spectral efficiency and BER performance.

## Slide 50: Experimental results for the mm-wave SEFDM-3
Bit rate (Gbit/s) measurements
SEFDM results in better throughput in both net and gross bit rates.
Gross bit rate: Achievable non-error bits per second including overhead.
Net bit rate: Achievable non-error bits per second without overhead.
A lower order modulation format 4QAM shows higher bit rate than a higher order format 8QAM over the same bandwidth.

## Slide 51: SEFDM Signals Transmission over the E-band
H. Ghannam, D. Nopchinda, M. Gavell, H. Zirath, and I. Darwazeh. Experimental Demonstration of Spectrally Efficient Frequency Division Multiplexing Transmissions at E-Band. IEEE Transactions on Microwave Theory and Techniques, 67(5):1911–1923, March 2019.

## Slide 52: Broadband Amplifiers with 200 GHz + BW
K. Eriksson, I. Darwazeh and H. Zirath, " InP DHBT Distributed Amplifiers With Up to 235-GHz Bandwidth", IEEE Transactions on Microwave Theory and Techniques, Vol. 63, Issue 4, pp. 1334-1341, April 2015.

## Slide 53: Wireless: E-band (82-68 GHz) UCL Collaboration with Chalmers University and Gotmic-Sweden
8 Gbit/s and BW reduced from 4 GHz to 2.67 GHz
Notes: A detailed description of the experiment setup is referred to the un-submitted CO-SEFDM PTL paper.

## Slide 54: 60 GHz mm-wave Radio Over Fiber SEFDM
[1]. S. Mikroulis, T. Xu, J. E. Mitchell and I. Darwazeh, ”First demonstration of a spectrally efficient FDM radio over fiber system topology for beyond 4G cellular networking,” in Networks and Optical Communications - (NOC), 2015 20th European Conference on, Jun. 2015, pp. 1–5.
[2]. S. Mikroulis, T. Xu, and I. Darwazeh, “Practical demonstration of spectrally efficient FDM millimeter-wave radio over fiber systems for 5G cellular networking,” in Proc. SPIE, vol. 9772, 2016, pp. 97 720I– 1–97 720I–8.
[3]. T. Xu, S. Mikroulis, J. E. Mitchell and I. Darwazeh, ” Bandwidth Compressed Waveform for 60 GHz Millimeter-Wave Radio over Fiber Experiment,” Lightwave Technology, Journal of. 2016.
85 GHz mm-wave SEFDM
Experimental Demonstration of Spectrally Efficient Frequency Division Multiplexing Transmissions at E-Band Hedaia Ghannam;Dhecha Nopchinda;Marcus Gavell;Herbert Zirath;Izzat Darwazeh IEEE Transactions on Microwave Theory and Techniques Year: 2019 | Volume: 67, Issue: 5

## Slide 55
Half-Sinc signal waveform
T. Xu and I. Darwazeh, “Half-Sinc Waveform Design for Narrowband IoT,” in IEEE 29th Annual International Symposium on Personal, Indoor, and Mobile Radio Communications (PIMRC), Bologna, Italy, Sept. 2018, pp. 600–601.

## Slide 56: Neural Network Topology Design
Conventional Detector Resource Map
Evolution
Possible AI Detector Resource Map
T. Xu, T. Xu, and I.Darwazeh, “Deep learning for interference cancellation in non-orthogonal signal based optical communication systems,” in IEEE Progress in Electromagnetics Research Symposium – Spring (PIERS), Toyama, Japan, Aug. 2018, pp. 241–248. (invited).

## Slide 57: Neural network prototyping on a SDR platform
Neural network weight compression
Principle of neural network training and detection
T. Xu and I. Darwazeh, “Design and prototyping of neural network compression for non-orthogonal IoT signals,” in 2019 IEEE Wireless Communications and Networking Conference (WCNC) (IEEE WCNC 2019), Marrakech, Morocco, Apr. 2019.

## Slide 58: MU-MIMO Precoding and Prototyping Platform
Architecture of precoding MU-MIMO systems
one-stage precoding MU-MIMO-OFDM
Frame and resource block structure for each antenna. One frame consists of 20 time slots and the first time slot is the overhead including SRS for downlink antenna spatial CSI estimation, which is used for space precoding at the transmitter. The locations of overhead from different antennas are staggered to avoid interference
T. Xu, C. Masouros, and I. Darwazeh, “Waveform and space precoding for next generation downlink narrowband IoT,” IEEE Internet of Things Journal, vol. 6, no. 3, pp. 5097–5107, Jun. 2019.

## Slide 59: Two-Stage Precoding
Waveform precoding can use offline precoding matrix
MIMO precoding has to use online feedback CSI
Balance of precoding performance and processing speed
T. Xu, F. Liu, A, Li, C. Masouros, and I. Darwazeh, “Constructive Interference Precoding for Reliable Non-Orthogonal IoT Signaling,” IEEE International Conference on Computer Communications (IEEE INFOCOM 2019), Paris, France, Apr. 2019, pp. 590–595.
Methods are available for the waveform and MIMO precoding:
Zero Forcing Precoding (ZF)
MMSE precoding (MMSE)
Singular Value Reconstruction (SVR)
Constructive Interference Precoding (CI)
World-first CI-MIMO-SEFDM system demo

## Slide 60: Hybrid analogue digital multi-user MIMO beamforming
T. Xu, C. Masouros, and I. Darwazeh, “Design and Prototyping of Hybrid Analogue Digital Multiuser MIMO Beamforming for Non-Orthogonal Signals,” IEEE Internet of Things Journal, vol. 7, no. 3, pp. 1872-1883, Mar. 2020

## Slide 61: Coexistence of waveforms
T. Xu and I. Darwazeh, “Experimental over-the-air testing for coexistence of 4G and a spectrally efficient non-orthogonal signal,” in IEEE 28th Annual International Symposium on Personal, Indoor, and Mobile Radio Communications (PIMRC), Montreal, QC, Canada, Oct. 2017, pp. 1–5.

## Slide 62: Coexistence of orthogonal and non-orthogonal signals
Orthogonal signalling
Non-Orthogonal
signalling
OFDM
FTN
FBMC
GFDM
UFMC
SEFDM
Coexistence
…
SEFDM
Data rate improvement
Bandwidth saving
Similar signal generation with OFDM
Easy integration in existing communication systems
Spectral Efficiency Improvement
Increase bit rate:
FTN
Reduce BW or increase bit rate
SEFDM
Coexistence advantage:
FBMC, GFDM, UFMC

## Slide 63: Broadband Amplifiers with 200 GHz + BW
K. Eriksson, I. Darwazeh and H. Zirath, " InP DHBT Distributed Amplifiers With Up to 235-GHz Bandwidth", IEEE Transactions on Microwave Theory and Techniques, Vol. 63, Issue 4, pp. 1334-1341, April 2015.

## Slide 64: Challenges
Does it work over different media (wireless and optical)?
Can it be made? SDR techniques; FPGAs; ICs
Practical problems?
Signal generation
Signal detection
Channel estimation
Amplifiers
Synchronisation
Frequency and phase offsets
Fit within existing standard waveforms and frames
Offer advantages over existing systems in real environments
A simple conclusion SEFDM:
Increase bit rate by up to 70% with power penalty (2-4 dB)
Or
Reduce transmission power for the same bit rate (up to 2 dB)
UK work started in 2003 now followed by 20+ groups worldwide and might be one of the comms standard modulation formats

## Slide 65: Acknowledgment Funding: EPSRC, Leverhulme, Cisco, ARM, NEC-Japan and Europe, Huawei
University College London
Dr Tongyang Xu
Ms Xinyue Liu
Professor Miguel Rodrigues
Dr Dhecha Nopchinda
Dr Ryan Grammenos
Professor John Mitchell
University College London-past
Dr Hedaia Ghannam
Dr Waseem Ozan
Dr Dimitrios Karampatsis
Dr Kai Li
Dr Ioannis Kanaras
Dr Safa Isam Ahmed
Dr Marcus Perrett
Dr Arsenia Chorti
Dr Paul Whatmough
Dr Spiros Mikroulis
Dr Benn Thomsen
Dr Paul Haigh
External collaboration
Professor Kyle Jamieson
Princeton University-USA
Professor Herbert Zirath
Chalmers University-Sweden
Professor Z Ghassemlooy
Northumbria University
Professor Farokh Marvesti
Sharif University-Iran
CSNDSP 2018